حملات به شبکه های محلی و راه های مقابله
کوشا اسماعیل پور
Koosha.id.ir
Koosha.es@gmail.com

---
MAC Flood
MAC Flood

---
macof
macof

---
DHCP starvation
DHCP starvation

---
Sending DISCOVER packet
Sending DISCOVER packet

---
Port Security
Port Security
- Switch(config)# interface interface_id
- Switch(config-if)# switchport mode access
- Switch(config-if)# switchport port-security
- Switch(config-if)# switchport port-security maximum value
- Switch(config-if)# switchport port-security violation {protect | restrict | shutdown }

---
VLAN hopping
VLAN hopping
- 1-Switch spoofing
- 2-Double tagging

---
1-Switch spoofing
1-Switch spoofing

---
Enabling trunking
Enabling trunking

---
1. Ensure that ports are not set to negotiate trunks automatically :
Switch(config-if)# switchport nonegotiate
OR
2. Ensure that ports that are not meant to be trunks are explicitly configured as access ports
Switch(config-if)# switchport mode access

---
Double tagging
Double tagging

---
Sending .1Q double encapsulation
Sending .1Q double encapsulation

---
Simply do not put any hosts on VLAN 1
Switch(config-if)# switchport access vlan 2
OR
Change the native VLAN on all trunk ports to an unused VLAN ID.
Switch(config-if)# switchport trunk native vlan 999
OR
Explicit tagging of the native VLAN on all trunk ports.
switch(config)# vlan dot1q tag native

---
STP Attack
STP Attack

---
Claiming Root Role
Claiming Root Role

---
BPDU guard OR Root guard
BPDU guard OR Root guard
- SW1(config)#interface interface_id
- SW1(config-if)#spanning-tree bpduguard enable
OR
- SW1(config)#interface interface_id
- SW1(config-if)#spanning-tree guard root

---
CDP Flood
CDP Flood

---
Disable or Turn Off CDP on Cisco
Switches & Routers
Disable or Turn Off CDP on Cisco
Switches & Routers
Router(config)# no cdp run
OR
- Router(config)# int interface_id
- Router(config-if)# no cdp enable

---
سال نو مبارک
سال نو مبارک